## Slide 1: ECE 484 - Advanced Digital Systems Design Lecture 10 – FPGA Design for Area, Power, or Speed
Capt Michael Tanner Room 2F46A 333-6766
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Documentation
Most of the images and notes in this presentation are taken from:
  Xilinx University Program [1]
  Xilinx Online FPGA Design Training [2]

## Slide 3: Lesson Outline
Xilinx FPGA Architecture
Optimizing for Area
Optimizing for Power
Optimizing for Speed

## Slide 4: Xilinx FPGA Architecture

## Slide 5: Xilinx FPGA Architecture Overview
Modern FPGA’s contain hardware-dedicated resources to for commonly used functions.
Improves performance
Reduces area and power use
7-Series Architecture Features
  Logic (“FPGA Fabric”)
  Interconnect
  Block/Distributed RAM
  SelectIO/CMT
  DSP Slices
  Serial Transceiver
SelectIO
& CMT
Logic
DSP
Serial Transceiver
BRAM
Clock Buffers and Routing
PCI Express
SelectIO
& CMT

## Slide 6: Xilinx FPGA Architecture CLB Structure
Two side-by-side slices per CLB
  Slice_M are memory-capable
  Slice_L are logic and carry only
Four 6-input LUTs per slice
  Consistent with previous architectures
  Single LUT in Slice_M can be a 32-bit shift register or 64 x 1 RAM (Distributed RAM)
Two flip-flops per LUT
  Excellent for heavily pipelined designs
CLB
SLICE
LUT
SLICE
LUT

## Slide 7: Xilinx FPGA Architecture Slice Structure
Local routing provides connection between slices in the same CLB, and it provides routing to neighboring CLBs
Carry logic runs vertically, between slices and CLBs
Other resources on slice:
  LUTs
  MUXs with dedicated routing
  Carry Logic
  Sequential Elements
Slice 0
LUT
Carry
LUT
Carry
D
Q
CE
PRE
CLR
D
Q
CE
PRE
CLR
Interconnect

## Slide 8: Xilinx FPGA Architecture Block RAM
Synchronous read and write capability
True dual-port memory
Built-in FIFO logic
Supports initial values and parity bits
Situated next to embedded multiplier for fast multiply-accumulate operations
36K/18K block RAM
  32k x 1 to 512 x 72 in one 36K block
  64-bit error correction coding per 36K block
  Adjacent blocks combine to 64K x 1 without extra logic
36
DIA
ADDRA
36
DOA
Port A
36 Kb Memory Array
CLKA
WEA
4
36
DIB
ADDRB
36
DOB
Port B
CLKB
WEB
4

## Slide 9: Xilinx FPGA Architecture Distributed RAM
Synchronous write
Asynchronous read – but can be made into synchronous read
RAM/ROM are initialized during configuration – data can be written to RAM after configuration
Emulated dual-port RAM
  One read/write port
  One read-only port
Implemented using LUTs
RAM16X1S
O
D
WE
WCLK
A0
A1
A2
A3
LUT
RAM32X1S
O
D
WE
WCLK
A0
A1
A2
A3
A4
RAM16X1D
SPO
D
WE
WCLK
A0
A1
A2
A3
DPRA0
DPO
DPRA1
DPRA2
DPRA3
Slice
LUT
LUT

## Slide 10: Xilinx 7-Series Architecture Input/Output Blocks (SelectIO)
Extension of logic layer functionality
  Wider input/output SERDES
  Addition of independent ODELAY
  Phaser, IO FIFO, IO PLL
Supports dozens of IO standards
  Single (PCI, CMOS, TTL, I2C, etc.)
  Differential (TMDS, Display Port, etc.)
  Tri-state buffers
  Double Data Rate
  Registered I/O
  Various Voltage levels
Reg
Reg
DDR MUX
3-state
OCK1
OCK2
Reg
Reg
DDR MUX
Output
OCK1
OCK2
PAD
Reg
Reg
Input
ICK1
ICK2
IOB

## Slide 11: Xilinx FPGA Architecture CMT/DCM
Former: Digital Clock Manager (DCM)
Current: Clock Management Tile (CMT)
Purpose:
  Reduce clock skew through feedback (PLL/DLL)
  Generate new frequencies that are a multiple/divisor of current frequency (e.g. clk*4/8)
  Phase shift clock
  Dedicated routing to all flip flops in within clock region to minimize clock skew

## Slide 12: Xilinx FPGA Architecture DSP Slice
7-Series Architecture DSP Slice Features:
  25x18 multiplier
  25-bit pre-adder
  Flexible pipeline
  Cascade in and out
  Carry in and out
  96-bit MACC
  SIMD support
  48-bit ALU
  Pattern detect
  17-bit shifter
  Dynamic operation (cycle by cycle)

## Slide 13: Xilinx FPGA Architecture Other Features
High-Speed Serial I/O Transceivers
Physical Layer
Data Link Layer
Transaction Layer
Configuration module
PCI Express Block
GTX Transceivers
17 External
Analog Inputs
On-Chip Sensors Supplies ±1%
Temperature ±4°C
ADC 1
MUX
ADC Results
XADC
Arbitrator
DRP
Dynamic Reconfiguration Port
Define XADC Operation
Initialize with Attributes
ADC 2
2 x 12 Bits
1 MSPS
Interconnect
JTAG
Status Registers
Control Registers
On-Chip Sensors
High-Speed Analog-to-Digital Converters

## Slide 14: Optimizing for Area

## Slide 15: Optimizing for Area
Use RTL design methodology
Use dedicated hardware when available (e.g., block RAM, multipliers, DSP, SERDES I/O, etc.)
Pay attention to synthesizer messages (e.g., could not infer block/distributed RAM due to a coding style mistake)
“Optimize for Area” during synthesis and implementation
  Resource Sharing
  Use IOB’s registers
  Combine LUTs
  Do not preserve hierarchy (do this last and only if needed)
“Optimize for Area” when using CoreGen tools
Use resets only when necessary, use synchronous resets
http://www.xilinx.com/itp/xilinx10/isehelp/ise_c_xst_area_reduction_strategies.htm

## Slide 16: Optimizing for Power

## Slide 17: Optimizing for Power
Minimize your dynamic power (see below equation)
Turn off parts of FPGA that aren’t in use
  Block RAM
  Use the Chip Enable signals for flip-flops
Use Xilinx tools to estimate power usage for various settings
“Optimize for Power” during synthesis and implementation
“Optimize for Power” when using CoreGen tools
Use resets only when necessary, use synchronous resets
http://www.xilinx.com/support/documentation/white_papers/wp285.pdf
n = number of toggling nodes
C = capacitance
V = voltage swing
f = toggle frequency

## Slide 18: Optimizing for Power

## Slide 19: Optimizing for Speed

## Slide 20: Optimizing for Speed Use Global Timing Constraints
With global timing constraints
  All timing paths are evaluated
  I/O paths are improved (CLBs are place closer to I/O pins)
Without global timing constraints
  Logic tends to be grouped to improve internal timing at the expense of I/O timing

## Slide 21: Optimizing for Speed Logic Levels and Delay
Enter your timing constraints into the Xilinx Constraints File
Over-constraining does not help you, but it will take longer to implement (if it can implement)
Review the timing reports after synthesis and implementation to see details (max clock speed, longest path, etc.)
Path endpoints are:
  I/O Pads
  Synchronous elements (FFs, Latches, RAMs, DSP slices, SRLs, etc.)
  NOT: LUTs, Nets, or any other asynchronous element
Global timing constraints will cover 90% of the timing constraints you need to deal with.
You can specify net-specific constraints, but that is beyond the scope of this class

## Slide 22: Optimizing for Speed Timing Constraints
The combination of the interconnect and the LUT forms a logic level
Lower speed grade devices operate slower (longer LUT delays)
50/50 rule is typically used – 50% of delay is from LUT, 50% from routing delay
Make your designs parallel - cascading logic (e.g., priority multiplexer) significantly slows down your design
Pipeline your design to reduce longest path and therefore increase maximum clock speed.
I3
I1
I2
I0
O
LUT4
0.5
I1
I2
I0
O
LUT3
0.5
I3
I1
I2
I0
O
LUT4
0.5
I1
I0
O
LUT2
0.5
1.4
1.5
2.1
1.6
1.8
1.9

## Slide 23: Optimizing for Speed PERIOD constraint
The PERIOD constraint covers paths between synchronous elements on a single clock domain
  In this example, there is one clock signal (CLK)
  There are five synchronous elements (all FFs) attach to the clock which means there are five path endpoints, in this case
  There are three delay paths constrained between those five FFs
Q
FLOP1
D
Q
FLOP3
D
BUFG
CLK
ADATA
OUT2
OUT1
Q
FLOP5
D
Q
FLOP4
D
BUS [7..0]
CDATA
Q
FLOP2
D
NET "clk" PERIOD = 20 ns;

## Slide 24: Optimizing for Speed OFFSET IN/OUT constraints
The OFFSET IN constraint covers paths from input pads to synchronous elements
The OFFSET OUT constraint covers paths from synchronous elements to input pads
OFFSET = IN 10 ns BEFORE "clk";
OFFSET = OUT 10 ns BEFORE "clk";
= Combinatorial Logic
CLK
ADATA
OUT2
OUT1
Q
FLOP
D
Q
FLOP
D
Q
FLOP
D
Q
FLOP
D
BUS [7..0]
CDATA
Q
FLOP
D
BUFG
OFFSET IN
OFFSET OUT

## Slide 25: Lesson Outline
Xilinx FPGA Architecture
Optimizing for Area
Optimizing for Power
Optimizing for Speed