## Slide 1: ECE 484 - Advanced Digital Systems Design Lecture 11 – Register Transfer Methodology
Capt Michael Tanner Room 2F46A 333-6766
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Introduction
Overview of FSMD
FSMD Design of a Repetitive-Addition Multiplier
Timing and Performance Analysis of FSMD
Synthesis Guidelines

## Slide 3: Introduction

## Slide 4: Introduction
How to realize an algorithm in hardware?
Two characteristics of an algorithm:
  Use of variables (symbolic memory location) Example: n = n + 1 (when programming in C)
  Sequential execution (execution order is important)

## Slide 5: Dataflow Implementation
“Dataflow” implementation in VHDL
  Convert the algorithm in to combinational circuit
  No memory elements
  The sequence is embedded into the “flow of data”
Problems with dataflow implementation:
  Can only be applied to trivial algorithm
  Not flexible
    Can we just share one adder in a time-multiplexing fashion to save hardware resources
    What happen if input size is not fixed (i.e., size is determined by an external input)

## Slide 6: Dataflow Example
Algorithm:
  Sum 4 numbers
  Divide the result by 8
  Round the final result
sum <= 0;
sum0 <= a(0);
sum1 <= sum0 + a(1);
sum2 <= sum1 + a(2);
sum3 <= sum2 + a(3);
q <= "000" & sum3(8 downto 3);
r <= "00000" & sum3(2 downto 0);
outp <= q + 1 when (r > 3) else
q;
size = 4;
sum = 0;
for i in (0 downto size-1) do
sum = sum + a(i);
q = sum / 8;
r = sum rem 8;
if (r > 3)
q = q+1;
outp = q;

## Slide 7: Register Transfer Methodology
Realized algorithm in hardware
Use register to store intermediate data and imitate variable
Use a datapath to realize all register operations
Use a control path (FSM) to specify the order of register operation
The system is specified as sequence of data manipulation/transfer among registers
Realized by FSM with a datapath (FSMD)

## Slide 8: Overview of FSMD

## Slide 9: Overview of FSMD
Basic form:
Interpretation:
  At the rising edge of the clock, the output of registers , , etc. are available
  Outputs are passed to a combinational circuit that performs
  At the next rising edge of the clock, result is stored into

## Slide 10: Implementation Example Single RT Operation

## Slide 11: Implementation Example Multiple RT Operations

## Slide 12: FSM as a Control Path
FSM is a good to control RT operation
  State transition is on clock-by-clock basis
  FSM can enforce order of execution
  FSM allows branches on execution sequence
Normally represented in an extended ASM chart known as ASMD (ASM with datapath) chart
Note: New value or is only available when the FSM exits state.

## Slide 13: Basic Block Diagram of FSMD

## Slide 14: FSMD Design of a Repetitive-Addition Multiplier

## Slide 15: FSMD Design Repetitive-Addition Multiplier
Basic algorithm: 7*5 = 7+7+7+7+7
Pseudo code:
ASMD-Friendly Code:
if ((a_in = 0) or (b_in = 0)) then
r = 0;
else
a = a_in;
n = b_in;
r = 0;
op: r = r + a;
n = n-1;
if (n = 0)
goto stop;
else
goto op;
stop: return r;
if ((a_in = 0) or (b_in = 0)) then
r = 0;
else
a = a_in;
n = b_in;
r = 0;
while (n != 0)
r = r + a;
n = n - 1;
return r;

## Slide 16: FSMD Design Repetitive-Addition Multiplier
Input:
  a_in, b_in: 8-bit unsigned
  clk, reset
  start: command
Output:
  r: 16-bit unsigned
  ready: status
ASMD chart
  Default RT operation: keep the previous value
  Note the parallel execution in op state
if ((a_in = 0) or (b_in = 0)) then
r = 0;
else
a = a_in;
n = b_in;
r = 0;
op: r = r + a;
n = n-1;
if (n = 0)
goto stop;
else
goto op;
stop: return r;

## Slide 17: FSMD Design Repetitive-Addition Multiplier
Construction of the data path
  List all RT operations
  Group RT operation according to the destination register
  Add combinational circuit/mux
  Add status circuits
RT operations with the
  r register
    (in the idle state)
    (in the load and op states)
    (in the op state)
  n register
    (in the idle state)
    (in the load and ab0 states)
    (in the op state)
  b register
    (in the idle and op states)
    (in the load and ab0 states)

## Slide 18: FSMD Design Repetitive-Addition Multiplier
Circuit associated with r register:

## Slide 19: FSMD Design Repetitive-Addition Multiplier
VHDL Code
  multiplier.vhd
  Various code segments can be combined
  Should always separate registers from combinational logic
  May be a good idea to isolate the main functional units

## Slide 20: Timing and Performance Analysis of FSMD

## Slide 21: Timing and Performance Analysis of FSMD
Maximal clock rate
  More difficult to analyze because of two interactive loops
  The boundary of the clock rate can be found
Best-case scenario:
  Control signals needed at late stage
  Status signal available at early stage

## Slide 22: Timing and Performance Analysis of FSMD

## Slide 23: Timing and Performance Analysis of FSMD
Performance of FSMD
  Tc: Clock period
  K: # clock cycles to compete the computation
  Total time = K * Tc
K determined by algorithm, input patterns, etc.
Example:
  8-bit input
    Best: b=0, K=2
    Worst: b=255, K=2 + 255*2
  N-bit input:
    Worst: K=2+2*(2n-1)

## Slide 24: Synthesis Guidelines

## Slide 25: Synthesis Guidelines
As with any sequential circuit, the registers of the FSMD should be separated from the combinational circuits.
Be aware that an RT operation exhibits a delayed-store behavior. Use of a register in a decision box should be carefully examined.
The variables used in Boolean expressions of a pseudo algorithm normally correspond to the next values of the registers used in an ASMD.
The function units are normally the most dominant components in a FSMD design. To exercise more control, we may need to isolate them from the rest of the code.
Separate the control path from the code if FSM optimization is needed later.

## Slide 26: Lesson Outline
Introduction
Overview of FSMD
FSMD Design of a Repetitive-Addition Multiplier
Timing and Performance Analysis of FSMD
Synthesis Guidelines