## Slide 1: ECE 484 - Advanced Digital Systems Design Lecture 4 – Combinational Circuits in VHDL
Capt Michael Tanner Room 2F46A 333-6766
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Combinational vs. Sequential Circuits
Simple Signal Assignment
Conditional Signal Assignment
Selected Signal Assignment
Conditional vs. Selected Signal Assignment
Synthesis Guidelines

## Slide 3: Combinational vs. Sequential Circuits

## Slide 4: Combinational vs. Sequential Circuits
Combinational circuit:
  No internal state
  Output is a function of inputs only
  No latches/FFs or closed feedback loop
Sequential circuit:
  With internal state
  Output is a function of inputs and internal state
Sequential circuit to be discussed later

## Slide 5: Simple Signal Assignment

## Slide 6: Simple Signal Assignment
Simple signal assignment is a special case of conditional signal assignment
Syntax: signal_name <= projected_waveform; y <= a + b + 1 after 10 ns;
Timing info ignored in synthesis and δ-delay is used: signal_name <= value_expression;

## Slide 7: Simple Signal Assignment
Example simple signal assignments
  status <= '1';
  even <= (p1 and p2) or (p3 and p4);
  arith_out <= a + b + c - 1;
Implementation of last statement:

## Slide 8: BAD: Simple Assignment with Closed Feedback Loop
A signal appears in both sides of a concurrent assignment statement q <= ((not q) and (not en)) or (d and en);
Syntactically correct
Forms a closed feedback loop (i.e., infinite loop)
Should be avoided

## Slide 9: Conditional Signal Assignment

## Slide 10: Conditional Signal Assignment
Syntax
Examples
Conceptual implementation
  signal_name
  <= value_expr_1 when boolean_expr_1 else
  value_expr_2 when boolean_expr_2 else
  value_expr_3 when boolean_expr_3 else
  . . .
  value_expr_n

## Slide 11: Example: 4-to-1 Multiplexer
library ieee;
use ieee.std_logic_1164.all;
entity mux4 is
port(
a,b,c,d: in std_logic_vector(7 downto 0);
s: in std_logic_vector(1 downto 0);
x: out std_logic_vector(7 downto 0)
);
end mux4;
architecture cond_arch of mux4 is
Begin
x <= a when (s="00") else
b when (s="01") else
c when (s="10") else
d;
end cond_arch;

## Slide 12: Example: 2-to-22 Binary Decoder
library ieee;
use ieee.std_logic_1164.all;
entity decoder4 is
port(
s: in std_logic_vector(1 downto 0);
x: out std_logic_vector(3 downto 0)
);
end decoder4;
architecture cond_arch of decoder4 is
begin
x <= "0001" when (s="00") else
"0010" when (s="01") else
"0100" when (s="10") else
"1000";
end cond_arch;

## Slide 13: Conceptual Implementation
Syntax:
  signal_name
  <= value_expr_1 when boolean_expr_1 else
  value_expr_2 when boolean_expr_2 else
  value_expr_3 when boolean_expr_3 else
  . . .
  value_expr_n
Evaluation in ascending order
Achieved by “priority-routing network”
Top value expression has a “higher priority”

## Slide 14: 2-to-1 Mux Implementation
  signal_name <= value_expr_1 when boolean_expr_1 else
  value_expr_2

## Slide 15: Cascaded Mux Implementation
  signal_name <= value_expr_1 when boolean_expr_1 else
  value_expr_2 when boolean_expr_2 else
  value_expr_3 when boolean_expr_3 else
  value_expr_4

## Slide 16: Cascaded Mux Implementation

## Slide 17: Selected Signal Assignment

## Slide 18: Selected Signal Assignment
Syntax
Examples
Conceptual implementation
select_expression
  Discrete type or 1-D array
  With finite possible values
choice_i
  A value of the data type
Choices must be
  mutually exclusive
  all inclusive
  others can be used as last choice_i
with select_expression select
sig_name <= expr_1 when choice_1,
expr_2 when choice_2,
expr_3 when choice_3,
. . .
expr_n when choice_n;

## Slide 19: Example: 4-to-1 Multiplexer
Question: Can ‘when “11”’ be used to replace the ‘when others’ statement?
architecture sel_arch of mux4 is
begin
with s select
x <= a when "00",
b when "01",
c when "10",
d when others;
end sel_arch;

## Slide 20: Example: 2-to-22 Decoder
architecture sel_arch of mux4 is
begin
with s select
x <= "0001" when "00",
"0010" when "01",
"0100" when "10",
“1000" when others;
end sel_arch;

## Slide 21: Example: Simple ALU
architecture sel_arch of simple_alu is
signal sum: std_logic_vector(7 downto 0);
signal diff: std_logic_vector(7 downto 0);
signal inc: std_logic_vector(7 downto 0);
begin
inc <= std_logic_vector(
signed(src0) + 1 );
sum <= std_logic_vector(
signed(src0) + signed(src1) );
diff <= std_logic_vector(
signed(src0) - signed(src1) );
with ctrl select
result <= inc when "000"|"001"|"010"|"011",
sum when "100",
diff when "101",
src0 and src1 when "110",
src0 or src1 when others; -- "111“
end sel_arch;
Question: Can “0--” be used to replace the first statement?

## Slide 22: Conceptual Implementation
Achieved by a multiplexing circuit
Abstract (k+1)-to-1 multiplexer
  sel is with a data type of (k+1) values: c0, c1, c2, . . . , ck
select_expression is with a data type of 5 values: c0, c1, c2, c3, c4
with select_expression select
sig <= value_expr_0 when c0,
value_expr_1 when c1,
value_expr_n when others;

## Slide 23: Conceptual Implementation

## Slide 24: Conditional vs. Selected Signal Assignment

## Slide 25: Conditional vs. Selected Signal Assignment
Conversion between conditional vs. selected signal assignment
Comparison

## Slide 26: Conversion: Selected → Conditional
with sel select
sig <= value_expr_0 when c0,
value_expr_1 when c1|c3|c5,
value_expr_2 when c2|c4,
value_expr_n when others;
sig <=
value_expr_0 when (sel=c0) else
value_expr_1 when (sel=c1) or (sel=c3) or (sel=c5) else
value_expr_2 when (sel=c2) or (sel=c4) else value_expr_n;

## Slide 27: Conversion: Conditional → Selected
sig <= value_expr_0 when bool_expr_0 else
value_expr_1 when bool_expr_1 else
value_expr_2 when bool_expr_2 else
value_expr_n;
sel(2) <= '1' when bool_exp_0 else '0';
sel(1) <= '1' when bool_exp_1 else '0';
sel(0) <= '1' when bool_exp_2 else '0';
with sel select
sig <= value_expr_0 when "100"|"101"|"110"|"111",
value_expr_1 when "010"|"011",
value_expr_2 when "001",
value_expr_n when others,

## Slide 28: Conditional vs. Selected Comparison
Selected signal assignment:
  Good match for a circuit described by a functional table
  Example: binary decoder, multiplexer
  Less effective if input pattern is given a preferential treatment
Conditional signal assignment:
  good match for a circuit a circuit that needs to give preferential treatment for certain conditions or to prioritize the operations
  Example: priority encoder
  May “over-specify” for a functional table based circuit.
  Can handle complicated conditions.
pc_next <=
pc_reg + offset when (state=jump and a=b) else
pc_reg + 1 when (state=skip and flag='1') else
...

## Slide 29: Synthesis Guidelines

## Slide 30: Synthesis Guidelines
Avoid a closed feedback loop in a concurrent signal assignment statement.
Think of the conditional signal assignment and selected signal assignment statements as routing structures rather than sequential control constructs.
The conditional signal assignment statement infers a priority routing structure, and a larger number of when clauses leads to a long cascading chain.
The selected signal assignment statement infers a multiplexing structure, and a large number of choices leads to a wide multiplexer.

## Slide 31: Lesson Outline
Combinational vs. Sequential Circuits
Simple Signal Assignment
Conditional Signal Assignment
Selected Signal Assignment
Conditional vs. Selected Signal Assignment
Synthesis Guidelines