## Slide 1: ECE 484 - Advanced Digital Systems Design Lecture 7 – Hierarchical and Testable Design in VHDL
Capt Michael Tanner Room 2F46A 333-6766
HQ U.S. Air Force Academy
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
Notes: Write on board:
ECE 315
Day 1 – Admin
Section Marcher
Introductions
Syllabus

## Slide 2: Lesson Outline
Introduction
Components
Generics
Configuration
Other Supporting Constructs
Synthesis Guidelines

## Slide 3: Introduction

## Slide 4: Introduction
How to deal with 1 Million gates or more?
Hierarchical design
  Divided-and-conquer strategy
  Divide a system into smaller parts
Sequential Multiplier
Control Path
Data Path
State Register
Next-State Logic
Data Register
Functional Units
Adder
Decrementor
Routing Network

## Slide 5: Benefits of Hierarchical Design
Complexity management
  Focus on a manageable portion of the system, and analyze, design and verify each module in isolation.
  Construct the system in stages by a designer or concurrently by a team of designers.
  Help synthesis process
Design reuse
  Use predesigned modules or third-party cores
  Use the same module in different design
  Isolate device-dependent components (e.g., SRAM)

## Slide 6: Relevant VHDL Constructs
Component
Generic
Configuration
Library
Package
Subprogram

## Slide 7: Components

## Slide 8: Components
Hierarchical design usually shown as a block diagram (structural description)
VHDL component is the mechanism to describe structural description in text
To use a component
  Component declaration (make known)
    Instantiate an instance of a component
    Provide a generic value
    Map formal signals to actual signals
  Component instantiation (create an instance)
    Instantiate an instance of a component
    Provide a generic value
    Map formal signals to actual signals
component component_name
generic(
generic_declaration;
generic_declaration;
);
port(
port_declaration;
port_declaration;
);
end component;
instance_label: component_name
generic map(
generic_association;
generic_association;
)
port map(
port_association;
port_association;
);

## Slide 9: Components
-- Before “begin”
component dec_counter is
port(
clk, reset : in std_logic;
q : out std_logic_vector(3 downto 0);
pulse : out std_logic
);
end component;
Port association (named association – formal to actual parameters) port_name => signal_name
Positional association – order of port declaration in entity
  Appeared to be less cumbersome
  Alternative component instantiation
  Trouble if the order later changes in entity declaration
entity dec_counter is
port(
clk, reset : in std_logic;
q : out std_logic_vector(3 downto 0);
pulse : out std_logic
);
end dec_counter;
-- In the body
one_digit: dec_counter
port map(
clk => clk,
reset => reset,
q => q_one
);

## Slide 10: Mapping of constant and Unused Ports
Good synthesis software should
  remove the unneeded part
  perform optimization over the constant input
-- In the body
one_digit: dec_counter
port map(
clk => clk,
reset => reset,
en => ‘1',
pulse => p_one,
q => q_one
);
ten_digit: dec_counter
port map(
clk => clk,
reset => reset,
en => p_one,
pulse => open,
q => q_one
);
If you do not need a port, use the open keyword

## Slide 11: Generics

## Slide 12: Generics
Mechanism to pass info into an entity/component
Declared in entity declaration and then can be used as a constant in port declaration and architecture body
Assigned a value when the component is instantiated.
Like a parameter, but has to be constant
Can be used in port declaration
entity para_binary_counter is
generic(WIDTH: natural);
port(
clk, reset: in std_logic;
q: out std_logic_vector(WIDTH-1 downto 0)
);
end para_binary_counter;
architecture arch of para_binary_counter is
signal r_reg : unsigned(WIDTH-1 downto 0);
signal r_next : unsigned(WIDTH-1 downto 0);
begin
process(clk, reset) is
begin
if (reset='1') then
r_reg <= (others => '0');
elsif (clk'event and clk='1') then
r_reg <= r_next;
end if; end process;
r_next <= r_reg + 1;
q <= std_logic_vector(r_reg);
end arch;

## Slide 13: Parameterized mod-n Counter
Count from 0 to n-1 and wrap around
Note that WIDTH depends on N
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity mod_n_counter is
generic(
N: natural;
WIDTH: natural
);
port(
clk, reset: in std_logic;
en: in std_logic;
q: out std_logic_vector(WIDTH-1 downto 0);
pulse: out std_logic
);
end mod_n_counter;
architecture arch of mod_n_counter is
signal r_reg: unsigned(WIDTH-1 downto 0);
signal r_next: unsigned(WIDTH-1 downto 0);
begin
process(clk,reset) -- register
begin
if (reset='1') then
r_reg <= (others=>'0');
elsif (clk'event and clk='1') then
r_reg <= r_next;
end if;
end process;
process(en,r_reg) -- next-state logic
begin
r_next <= r_reg;
if (en='1') then
if r_reg=(N-1) then
r_next <= (others=>'0');
else
r_next <= r_reg + 1;
end if;
end if;
end process;
-- output logic
q <= std_logic_vector(r_reg);
pulse <= '1' when r_reg=(N-1) else '0';
end arch;

## Slide 14: 2-Digit Decimal Counter
one_digit: dec_counter
generic map( N=>10, WIDTH=>4)
port map (
clk=>clk,
reset=>reset,
en=>'1',
pulse=>p_one,
q=>q_one
);
ten_digit: dec_counter
generic map( N=>10, WIDTH=>4)
port map (
clk=>clk,
reset=>reset,
en=>p_one,
pulse=>open,
q=>q_ten
);
p100 <= p_one and p_ten;

## Slide 15: Configuration

## Slide 16: Configuration
Bind a component with an entity and an architecture
Flexible and involved.
Only simple binding of entity and architecture is needed in synthesis
  Entity: like a socket in a printed circuit board
  Architecture: like an IC chip with same outline
Not supported by all synthesis software
Application of binding:
  Example: adder with different speed: Fast but large adder or small but slow adder
  Example: Test bench descriptions at different stages

## Slide 17: Configuration
Type of configuration:
  Configuration declaration (an independent design unit)
  Configuration specification (in architecture body)
Default binding: (no configuration)
  Component bound to an entity with identical name
  Component ports bound to entity ports of same names
  Most recently analyzed architecture body bound to the entity
Configuration declaration
  An independent design unit
  Simplified syntax
configuration conf_name of entity_name is
for architecture_name
for instance_label: component_name
use entity lib_name.bount_entity_name(bound_arch_name);
end for;
for instance_label: component_name
use entity lib_name.bount_entity_name(bound_arch_name);
end for;
...
end;

## Slide 18: Two Architecture Bodies
One body for up-counting, one body for down-counting
You create a new design unit that specifies how your entity (hundred_counter) will map for a given architecture (vhdl_87_arch):
configuration count_down_config of hundred_counter is
for vhdl_87_arch
for one_digit: dec_counter
use entity work.dec_counter(down_arch);
end for;
for ten_digit: dec_counter
use entity work.dec_counter(down_arch);
end for;
end;
architecture down_arch of dec_counter is

## Slide 19: Configuration Specification
Alternative to creating a new configuration design unit
Placed in the “declarations” of your structural VHDL architecture body
for instance_label : component_name
use entity lib_name.bound_entity_name(bound_arch_name);
for instance_label : component_name
use entity lib_name.bound_entity_name(bound_arch_name);
architecture vhdl_93_arch of hundred_counter is
component dec_counter is
port(
clk, reset, en : in std_logic;
q : out std_logic_vector(3 downto 0);
pulse : out std_logic
);
for one_digit : dec_counter
use entity work.dec_counter(down_arch);
for ten_digit : dec_counter
use entity work.dec_counter(down_arch);
signal p_one, p_ten : std_logic;
begin
...

## Slide 20: VHDL 1993 Shortcut
Remove component and configuration declaration
Usually satisfactory for RT-level synthesis
instance_label:
entity lib_name.bound_entity_name(bound_arch_name)
generic map (...)
port map (...);
architecture vhdl_93_arch of hundred_counter is
signal p_one, p_ten : std_logic;
begin
one_digit: entity work.dec_counter(up_arch)
port map (clk => clk, reset => reset, en => en,
pulse => p_one, q => q_one);
ten_digit: entity work.dec_counter(up_arch)
port map (clk => clk, reset => reset, en => p_one,
pulse => p_ten, q => q_ten);
p100 <= p_one and p_ten;
end vhdl_93_arch;

## Slide 21: Other Supporting Constructs

## Slide 22: Other Supporting Constructs
Library
Subprogram
Package

## Slide 23: Library
A virtual repository to stored analyzed design units
Physical location determined by software
Design units can be organized and stored in different libraries
Default library: “work”
Non-Default library has to be declared (e.g. IEEE)
library ieee;
use entity work.dec_counter(down_arch);

## Slide 24: Subprogram
Include function and procedure
Made of sequential statement
Is not a design unit; must be declared
Aimed for software hierarchy not hardware hierarchy
We only use function
  Shorthand for complex expression
  “House-keeping tasks; e.g., type conversion
function func_name(parameter_list) return data_type is
declarations;
begin
sequential statement;
sequential statement;
...
end func_name;

## Slide 25: Example Subprogram
function log2c(n: integer) return integer is
variable m, p: integer;
begin
m := 0;
p := 1;
while p < n loop
m := m + 1;
p := p * 2;
end loop;
return m;
end log2c;

## Slide 26: Package
Organize and store declaration information, such as data types, functions etc.
Divided into
  Package declaration
  Package body (implementation of subprograms)
Both are design units
package body package_name is
subprogram or data type;
subprogram or data type;
...
end package_name;
package package_name is
declaration_item;
declaration_item;
...
end package_name;

## Slide 27: Package Example
-- Package Declaration
library ieee;
use ieee.std_logic_1164.all;
package util_pkg is
type std_logic_2d is
array(integer range <>, integer range <>) of std_logic;
function log2c (n: integer) return integer;
end util_pkg ;
-- Package Body
package body util_pkg is
function log2c(n: integer) return integer is
variable m, p: integer;
begin
m := 0;
p := 1;
while p < n loop
m := m + 1;
p := p * 2;
end loop;
return m;
end log2c;
end util_pkg;

## Slide 28: Partition
Physical partition:
  Division of the physical implementation
  Each subsystem is synthesized independently
Partition too small: loose optimization opportunity
Partition too large: require too much resource
  e.g., O(n3) algorithm 1000 gates for 1 sec;
  35 hours (503 sec) for one 50,000 gate circuit
  21 min (10*53 sec) for 10 5,000 gate circuit
5,000 to 50,000 gates for modern synthesizer

## Slide 29: Partition
Logical partition:
  Help development and verification process for human designers
  Logical partitions can be merged later in synthesis
Some circuit should be isolated as independent modules
  Device-dependent circuit: e.g., memory modules
  “Non-Boolean” circuit: tri-state buffer, delay-sensitive circuit, clock distribution network, synchronization circuit.

## Slide 30: Synthesis Guidelines

## Slide 31: Synthesis Guidelines
Use components, not subprograms, to specify the design hierarchy.
Use the std_logic and std_logic_vector data types in the ports of components to maintain portability.
Use named association, not positional association, in port mapping and generic mapping.
List all ports of a component in port mapping and use open for unused output ports.
For synthesis, partition the system into 5,000 – 50,000-gate modules. Collapse and flatten low-level hierarchy if the components are too small.
Separate device-dependent parts from ordinary logic and instantiate them as components in a hierarchy.
Separate non-Boolean circuits from ordinary logic and instantiate them as components in a hierarchy.

## Slide 32: Lesson Outline
Introduction
Components
Generics
Configuration
Other Supporting Constructs
Synthesis Guidelines